## Slide 1: H&P Computer Architecture A Quantitative Approach : Chapter 1.1 to 1.6
OMULUBI BRYSON FIBANDA
SCT212-0075/2020
COMPUTER TECHNOLOGY
4.2

## Slide 2: 1.1 Introduction
The journey of computers.
Performance increased from 25% per year (prior to mid 1980s) to 52% per year (1980s-2002) due to architectural innovations.
Key innovations:
Microprocessors - Made improvements to the integrated circuit tech leading to about 35% growth per year.
Led to creation of UNIX and Linux which lowered cost of introducing new architecture.
RISC Architecture - (Reduced Instruction Set Computers ) Raised the performance bar.
Switch from Instruction-Level Parallelism (ILP) to Thread-Level Paralelism (TLP) and Data Level Parallelism (DLP).
By 2002, computers became 7x faster than those of the mid-1980s.
Post-2002: Shift from single-core processors to multi-core processors due to power and performance limitations.

## Slide 3: 1.2 Classes of Computers
Evolution of Computer types from large mainframes which were used for business data processing and large scale scientific computing. The next innovation was minicomputers, supercomputers,desktop computers leading to the making of server-computers.
In the 90s, the internet and PDAs came along and became popular from 2000.
Major classes of computers:
Desktop Computers
Performance focused (Graphics, Processing Speed).
Cost range: $500 - $5000.
Servers
High-performance machines for businesses.
Made popular by the World Wide Web.
Focus on dependability, reliability, scalability, efficiency, cost-effectiveness and throughput.
Critical for websites like Amazon, eBay, and Google.

## Slide 4
Embedded Computers
Fast growing.
Hidden inside devices like phones, cars, and appliances.
Cost-effective, small, and power-efficient.
Real-time processing (e.g., video games).
Cost range between $5 and $100.
Personal Mobile Devices (PMDs): Smartphones and tablets, where power efficiency and size are key.
Warehouse-Scale Computers (WSCs): Large clusters of servers for cloud-based services.

## Slide 5: 1.3 Defining computer architecture
Computer architecture goes beyond just instruction sets. It involves designing how a computer's components interact, including logic design, memory systems, and power management.
The Instruction Set Architecture (ISA) defines the interface between software and hardware, but modern architecture must consider energy efficiency, cost, and performance.
Computer designer : Maximize computer performance and stay within cost, power and availability constraints.
Design aspects : Instruction set design, functional organization,logic design and implementation.
Implementation : Integrated circuit design,packaging, power and cooling.
Computer architecture is more than just the instruction set. It involves:
Instruction Set Architecture (ISA): How software interacts with hardware.
Seven dimensions of ISA: Class of ISA, Memory addressing, addressing modes, types and sizes of operands, operations, control flow instructions and encoding an ISA.

## Slide 6
Organization: How components like memory and CPU are arranged.
Hardware: Physical components like chips and transistors.
Modern architecture focuses on:
Power efficiency
Speed
Scalability
Compatibility with operating systems.

## Slide 7: 1.4 Trends in Technology
Critical modern implementations :
Integrated circuit technology : Density increases by 35% annually in transisitors.
Semiconductor DRAM (Memory): Doubles every 2 years. Increases by about 40%.
Magnetic Disks: Data storage improves by 30-100% per year.
Networks: Depends on performance of switches and transmission sysytem.
Key Design Consideration:
Design for future technologies that will be available by the time the product is released.
Performance trends :
Bandwith and Latency :
Bandwith grows by at least the square of the improvement in latency.
Scaling Transistor Performance and Wires:
Transistors improve with decrease in size.
As size reduces, wires get shorter and resistance and capacitance gets worse.

## Slide 8
Key trends:
Transistor Density (Moore's Law): Chips are getting smaller, faster, and more powerful.
Memory Technologies: DRAM and Flash memory are improving but at slower rates.
Magnetic Disks: Storage capacities grow, but performance improvements lag behind other components.

## Slide 9: 1.5 Trends in power in integrated circuits
Early microprocessors consumed less than a watt, but modern ones can reach 130 watts.
Techniques like dynamic voltage scaling and clock gating help manage power, but energy efficiency remains a critical concern.
Power as a critical factor in computer design:
Dynamic Power: Power used when transistors switch states.
Static Power: Power consumed even when transistors are off (leakage current).
Solutions to Reduce Power Consumption:
Lowering voltage.
Clock frequency lowering.
Turning off the clock of inactive modules.
Using multi-core processors at lower clock speeds
By 2006, leakage power accounted for 25% of total power consumption in processors.

## Slide 10: 1.6 Trends in Cost
The cost of integrated circuits is influenced by manufacturing complexity, volume, and time.
Higher volumes lead to lower prices, but design complexity and cutting-edge technology can increase costs. Commoditization - Standardized parts become cheaper over time.
Factors that influence computer cost:
Manufacturing Volume: Higher production reduces costs.
Learning Curve: Yield improves over time, lowering costs.
Components : Standard parts like RAM and disks are cheaper due to competition.
Integrated Circuit Costs:
Larger chips are more expensive to manufacture and have lower yields.
Example: A chip with 2.25 cm² size costs almost 4x more than a 1 cm² chip.